## Slide 1
Efficient 12-Lead ECG Reconstruction from Reduced Lead Sets
A Computationally Lightweight Physics-Informed Approach
Damilola Olaiya • Mithun Mani
DATA 5000 | Carleton University | December 2025

## Slide 2
The Clinical Need
▸ Cardiovascular Disease: #1 cause of death globally
  17.9 million deaths annually
▸ 12-Lead ECG: Gold standard diagnosis
  But requires 10 electrodes + trained personnel
▸ The Gap:
  Consumer wearables: only 1-3 leads
  Full diagnosis needs all 12 leads
▸ Our Goal: Reconstruct 12 leads from 3

## Slide 3
Key Insight: Physics Reduces the Problem
▸ The 12 leads are NOT independent!
▸ ✓ 4 Leads are EXACT (Physics):
  III = II - I (Einthoven 1903)
  aVR, aVL, aVF (Goldberger)
▸ ✓ Only 5 Leads Need Deep Learning:
  V1, V2, V3, V5, V6
▸ Result:
  Zero parameters for 4 leads
  Perfect reconstruction guaranteed
  6x fewer params than SOTA

## Slide 4
Hybrid Architecture
▸ Input: 3 leads (I, II, V4)
▸ Physics Module:
  Einthoven + Goldberger laws
  → 4 leads, r = 1.0, zero cost
▸ Deep Learning Module:
  1D U-Net (encoder-decoder)
  17.1M parameters
  → 5 chest leads
▸ Total: Complete 12-lead ECG

## Slide 5
Rigorous Methodology
▸ Frozen Hyperparameters (LR-validated):
  lr = 3×10⁻⁴, batch = 128, epochs = 150
  AdamW + ReduceLROnPlateau
▸ Patient-Wise Data Splits:
  No data leakage between train/test
  Stricter than most prior work
▸ Statistical Framework:
  Paired t-test, Cohen's d effect size
  Bootstrap 95% CI

## Slide 6
Dataset: PTB-XL
▸ 21,837 clinical 12-lead ECGs
▸ 18,885 unique patients
▸ 500 Hz, 10 seconds
▸ Train: 14,363 | Val: 1,914 | Test: 1,932
▸ Preprocessing:
  Z-score normalization
  Patient-wise stratified splits

## Slide 7
Training Convergence
[Figure: training_curves_final.png] Generate after training completes
Smooth convergence with ReduceLROnPlateau scheduler

## Slide 8
Overall Performance
r = 1.0
Physics Leads (III, aVR, aVL, aVF)
r = 0.82
DL Leads (V1-V3, V5-V6)
r = 0.93
Overall 12-Lead

## Slide 9
Per-Lead Performance
[Figure: per_lead_barplot.png] Generate after training completes
Physics leads perfect, DL leads V5 best (closest to V4), V2 hardest

## Slide 10
Sample ECG Reconstructions
[Figure: reconstruction_samples.png] Generate after training completes
Visual comparison: Ground truth (blue) vs Reconstructed (red)

## Slide 11
Ablation: Shared vs Lead-Specific Decoder
▸ Surprising Result:
  Shared (17.1M) BEATS Lead-Specific (40.8M)
▸ Statistical Evidence:
  Cohen's d = 0.92 (large effect)
  Bootstrap 95% CI: [0.006, 0.072]
  → Excludes zero = significant
▸ Interpretation:
  Limited input (3 leads) = limited information
  More params → overfitting, not capacity
  Parameter sharing = beneficial regularization

## Slide 12
Why V2 is Hardest: Information Bottleneck
▸ Ground truth correlation V4 ↔ V2 = 0.36
  Fundamental limit, not model failure
▸ Best performance on V5 (r ≈ 0.87):
  V4 ↔ V5 correlation = 0.79
▸ Worst performance on V2 (r ≈ 0.72):
  V2 anatomically distant from V4
▸ Implication:
  Input lead selection matters more
  than model architecture

## Slide 13
Comparison with State-of-the-Art
Method | Year | DL Leads r | Params | Split
Linear (Frank) | 1970s | 0.70-0.75 | ~0 | N/A
CNN (Sohn) | 2020 | ~0.85 | ~30M | Record
LSTM (Lee) | 2021 | ~0.88 | ~60M | Record
Transformer | 2023 | ~0.90 | 100M+ | Record
Ours | 2025 | ~0.82 | 17.1M | Patient

## Slide 14
Honest Assessment
▸ Our Advantages:
  ✓ 6x fewer parameters (17M vs 100M)
  ✓ Physics leads perfect (r = 1.0)
  ✓ Stricter evaluation (patient-split)
▸ Our Limitations:
  △ DL leads slightly below SOTA
  △ Single dataset (PTB-XL only)
  △ Input config (I, II, V4) not optimized
▸ Key Insight:
  Gap may be due to stricter evaluation

## Slide 15
Key Contributions
▸ 1. Efficient Hybrid Architecture
  Physics + lightweight DL = 6x smaller
▸ 2. Rigorous Methodology
  Patient-wise splits, frozen HPs, stats tests
▸ 3. Information Bottleneck Analysis
  Identified fundamental reconstruction limits
▸ 4. Open Source
  github.com/whiteblaze143/DATA_5000

## Slide 16
Limitations & Future Work
▸ Current Limitations:
  Single dataset (PTB-XL)
  Input config not optimized
  No downstream task validation
▸ Future Directions:
  Test (I, II, V2) or (I, II, V2, V4)
  External validation (Chapman, MIMIC)
  Multi-label classification on reconstructed ECGs
  Uncertainty quantification

## Slide 17
Summary
17.1M (6x smaller)
Parameters
r = 1.0 (guaranteed)
Physics Leads
r ≈ 0.82 (patient-split)
DL Leads

## Slide 18
Code & Resources
▸ GitHub Repository:
  github.com/whiteblaze143/DATA_5000
▸ Key Files:
  run_training.py — Main entry
  src/physics.py — Einthoven/Goldberger
  src/models/unet_1d.py — 1D U-Net
▸ Trained Models & Report:
  models/final_exp_baseline/
  docs/PROJECT_REPORT.pdf

## Slide 19
Acknowledgments
▸ Course: DATA 5000 - Data Science Capstone
▸ Carleton University
▸ PhysioNet for PTB-XL dataset
▸ Google Cloud for compute resources

## Slide 20
?
Questions?

## Slide 21
Thank You!
Damilola Olaiya
damilolaolaiya@cmail.carleton.ca
Mithun Mani
mithunmani@cmail.carleton.ca
github.com/whiteblaze143/DATA_5000