## Slide 1
12-Lead ECG Reconstruction from Reduced Lead Sets
A Hybrid Physics-Informed Deep Learning Approach
Damilola Olaiya • Mithun Mani
DATA 5000 | Carleton University | December 2025

## Slide 2
01
THE PROBLEM

## Slide 3
The Clinical Problem
▸ Cardiovascular disease: #1 cause of death globally
  17.9 million deaths annually
▸ 12-lead ECG: Gold standard for cardiac diagnosis
  Detects arrhythmias, MI, conduction abnormalities
▸ The accessibility gap:
  Requires 10 electrodes + precise placement
  Needs trained technicians
  Difficult in ambulances, homes, remote areas
  Consumer wearables capture only 1-2 leads
Notes: The motivation is simple: 12-lead ECGs are clinically essential but practically inaccessible.

## Slide 4
Research Question
▸ Can we reconstruct a full 12-lead ECG
▸ from only 3 measured leads?
▸ Our key insight: The 12 leads aren't independent!
▸ 3 Input leads: Measured (I, II, V4)
▸ 4 Physics leads: Exact equations (III, aVR, aVL, aVF)
▸ 5 DL leads: Neural network (V1, V2, V3, V5, V6)
▸ Hybrid approach combines physics guarantees
▸ with deep learning flexibility

## Slide 5
02
METHODS

## Slide 6
The 12-Lead ECG System
12-lead ECG provides 12 different views of cardiac electrical activity
Notes: A lead isn't a wire—it's a viewpoint of heart activity.

## Slide 7
Physics Module: Exact Lead Derivation
Einthoven's Law (1903)
Lead III = Lead II − Lead I
Goldberger's Equation (aVR)
aVR = −(Lead I + Lead II) / 2
Goldberger's Equation (aVL)
aVL = Lead I − Lead II / 2
Goldberger's Equation (aVF)
aVF = Lead II − Lead I / 2
Notes: These equations guarantee r=1.0 correlation for 4 leads—no learning required!

## Slide 8
Physics Module: Perfect Reconstruction
1.000
Lead III Correlation
1.000
aVR Correlation
1.000
aVL Correlation
1.000
aVF Correlation
Notes: 4 of 12 leads reconstructed perfectly via physics—zero learned error!

## Slide 9
Neural Network: 1D U-Net Architecture
▸ Encoder-Decoder with Skip Connections
▸ Encoder Path (Downsampling):
  3 → 64 → 128 → 256 → 512 channels
  MaxPool1D reduces: 5000 → 312 timesteps
▸ Bottleneck: 1024 channels
  Captures multi-beat context
▸ Decoder Path (Upsampling):
  Skip connections preserve QRS spikes
  Output: [B, 5, 5000]

## Slide 10
Model Ablation: Shared vs Lead-Specific Decoder
Shared Decoder
17.1M params
vs
Lead-Specific
40.8M params
✓
Notes: Counter-intuitively, simpler model wins! Parameter sharing provides regularization.

## Slide 11
03
DATASET

## Slide 12
Dataset: PTB-XL
▸ Source: PhysioNet (publicly available)
▸ Total ECGs: 21,837
▸ Unique Patients: 18,885
▸ Sampling Rate: 500 Hz
▸ Duration: 10 seconds per recording
▸ Samples per Lead: 5,000
▸ Diagnostic labels (SNOMED-CT):
  MI, AF, LBBB, RBBB, LVH, etc.

## Slide 13
Patient-Wise Data Splitting (Critical!)
▸ The Problem:
  Some patients have multiple ECGs
  Record-wise split → same patient in train AND test
  Result: Data leakage → inflated metrics!
▸ Our Solution:
  Split by PATIENT ID, not by record
  Each patient in only ONE split
▸ Split Statistics:
  Train: 14,363 (70%)
  Validation: 3,086 (15%)
  Test: 3,086 (15%)
Notes: This is stricter than most prior work but gives honest generalization estimates.

## Slide 14
04
RESULTS

## Slide 15
Training Convergence
Model converges smoothly over 150 epochs with ReduceLROnPlateau scheduler

## Slide 16
Results: Deep Learning Leads
Lead | MAE | Correlation | SNR (dB)
V1 | 0.036 | 0.726 | 17.9
V2 (hardest) | 0.041 | 0.683 | 17.1
V3 | 0.036 | 0.765 | 17.8
V5 (best) | 0.032 | 0.824 | 18.7
V6 | 0.038 | 0.723 | 17.2
Mean | 0.037 | 0.744 | 17.8
Notes: V5 performs best (close to V4). V2 hardest (far from V4).

## Slide 17
Overall 12-Lead Performance
0.893
Overall Correlation
0.744
DL Leads Correlation
0.015
Overall MAE
Notes: Overall 0.893 is inflated by physics leads. Honest DL metric: 0.744

## Slide 18
Reconstruction Example: Ground Truth vs Predicted
Visual comparison of reconstructed ECG leads against ground truth

## Slide 19
Per-Lead Performance Analysis
Correlation varies by lead proximity to input V4

## Slide 20
05
ANALYSIS

## Slide 21
Information Bottleneck: Why V2 is Hard
V2 has only 0.36 ground truth correlation with V4 — fundamental limit on reconstruction

## Slide 22
Ground Truth Inter-Lead Correlations
Low V4↔V1/V2 correlation explains reconstruction difficulty for right precordial leads

## Slide 23
Comparison with State-of-the-Art
Method | Year | Chest r | Data Split
Linear (Frank) | 1970s | 0.70-0.75 | N/A
CNN (Sohn) | 2020 | 0.85 | Record-wise
LSTM (Lee) | 2021 | 0.88 | Record-wise
Transformer | 2023 | 0.90 | Record-wise
Ours | 2025 | 0.744 | Patient-wise
Notes: We're below SOTA but use stricter evaluation. Prior work may have data leakage.

## Slide 24
Gap Analysis: Why Below SOTA?
▸ Three factors explain the performance gap:
▸ 1. Patient-wise splitting (stricter, more honest)
  Prior work uses record-wise → data leakage
▸ 2. Input lead choice (I, II, V4)
  V4 has low correlation with V1/V2
  Information bottleneck limits reconstruction
▸ 3. No data augmentation or pretrained weights
✓ Our advantage: Physics guarantees + honest evaluation

## Slide 25
Key Findings
✓ Physics constraints work perfectly
  Limb leads: r = 1.0 guaranteed
✓ Simpler models win with limited input
  Shared decoder beats lead-specific by 5.3%
⚠ Information bottleneck is the fundamental limit
  V4 ↔ V2 correlation only 0.36
⚠ Input selection > model architecture
  Adding V2 as input would improve V2 reconstruction

## Slide 26
06
CONCLUSION

## Slide 27
Limitations
▸ Single Dataset
  Only PTB-XL tested — generalization unknown
▸ Resting ECGs Only
  No stress/exercise ECGs
▸ Input Lead Dependency
  Results specific to (I, II, V4) configuration
▸ No Downstream Validation
  Signal metrics only, no classification test
▸ No Uncertainty Quantification
  Point estimates only

## Slide 28
Future Directions
▸ Input Lead Optimization
  Test: (I, II, V2), (I, II, V3), (I, II, V2+V4)
▸ Uncertainty Quantification
  Add probabilistic head (VAE, MC Dropout)
▸ External Validation
  Chapman-Shaoxing, MIMIC-IV-ECG datasets
▸ Downstream Validation
  Multi-label classification on reconstructed ECGs
▸ Foundation Model Approach
  Self-supervised pretraining on millions of ECGs

## Slide 29
Summary
r = 1.0
Physics Leads
r = 0.744
DL Leads
r = 0.893
Overall
Notes: Hybrid approach: perfect physics + reasonable DL reconstruction

## Slide 30
Code & Resources
▸ GitHub Repository
  github.com/whiteblaze143/DATA_5000
▸ Key Files:
  run_training.py — Main entry point
  src/physics.py — Einthoven/Goldberger
  src/models/unet_1d.py — U-Net architecture
▸ Trained Model:
  models/overnight_full/best_model.pt
▸ Results:
  models/model_comparison_metrics.json

## Slide 31
?
Questions?

## Slide 32
Thank You!
Damilola Olaiya
damilolaolaiya@cmail.carleton.ca
Mithun Mani
mithunmani@cmail.carleton.ca
github.com/whiteblaze143/DATA_5000