## Slide 1
12-Lead ECG Reconstruction from Reduced Lead Sets
A Hybrid Physics-Informed Deep Learning Approach
Damilola Olaiya & Mithun Mani
DATA 5000 - Carleton University | December 2025

## Slide 2
The Clinical Problem
Cardiovascular disease: #1 cause of death globally (17.9M deaths/year)
12-lead ECG: Gold standard for cardiac diagnosis
  Detects arrhythmias, MI, conduction abnormalities, hypertrophy
The accessibility gap:
  Requires 10 electrodes + precise anatomical placement
  Needs trained technicians for proper acquisition
  Difficult in ambulances, homes, remote areas
  Consumer wearables (Apple Watch, Fitbit): only 1-2 leads
Research Question: Can we bridge this gap computationally?
Notes: The motivation is simple: 12-lead ECGs are clinically essential but practically inaccessible. Wearables capture 1-2 leads. Can we reconstruct the full 12-lead from minimal inputs?

## Slide 3
Our Approach: Hybrid Physics-Informed Deep Learning
Key Insight: The 12 leads aren't independent!
Decomposition into three groups:
  3 Input leads (I, II, V4): Measured directly
  4 Physics leads (III, aVR, aVL, aVF): Exact equations
  5 DL leads (V1, V2, V3, V5, V6): Neural network
Hybrid Pipeline:
  Input (3 leads) → Physics Module (4 exact) + U-Net (5 learned) → 12 leads
Advantage: Guarantee perfect reconstruction for 4 leads via physics
Notes: Our key insight is that not all leads need to be learned. Four limb leads can be computed exactly using 19th-century physiology. We only need deep learning for the 5 chest leads.

## Slide 4
Understanding ECG Leads
What is a 'lead'?
Not the wire—a VIEW of heart activity
Voltage difference between positions
Like viewing from different camera angles
12-Lead Breakdown:
Bipolar Limb: I, II, III
Augmented Limb: aVR, aVL, aVF
Precordial (Chest): V1-V6
Key Relationships:
Limb leads are mathematically related
Given I and II → derive III, aVR, aVL, aVF
Chest leads are independent
Must be measured or reconstructed
Positioned across the chest wall
V1-V2: Right side (septum)
V4-V6: Left side (lateral wall)
Notes: A lead isn't a wire—it's a viewpoint. The 12-lead ECG gives us 12 angles. Critically, the 6 limb leads are mathematically related, while chest leads capture unique horizontal plane information.

## Slide 5
Physics Component: Exact Lead Derivation
Lead III = Lead II − Lead I
Einthoven's Law (1903)
aVR = −(Lead I + Lead II) / 2
Goldberger's Equation
aVL = Lead I − Lead II / 2
Goldberger's Equation
aVF = Lead II − Lead I / 2
Goldberger's Equation
Notes: These equations come from Kirchhoff's voltage law applied to the body as a conductor. Given leads I and II, we compute the other four limb leads with perfect accuracy.

## Slide 6
Physics Module: Implications
Given I and II → derive III, aVR, aVL, aVF exactly
Properties:
  Zero learnable parameters
  Guaranteed r = 1.0 correlation
  No training required
  Works for ALL patients, ALL pathologies
This is the power of physics-informed ML:
  Eliminate learned error where deterministic solutions exist
  Use ML only where physics is insufficient
Code: src/physics.py
Notes: For the physics-based leads, we achieve perfect reconstruction by definition. This is the key advantage of our hybrid approach—we guarantee perfect results for 4 of 12 leads without any learning.

## Slide 7
The Deep Learning Challenge: Chest Leads
Problem: Chest leads V1-V6 have NO closed-form relationship to limb leads
Our Task:
  Input: 3 leads (I, II, V4) → tensor shape [B, 3, 5000]
  Output: 5 leads (V1, V2, V3, V5, V6) → tensor shape [B, 5, 5000]
  Formulation: Sequence-to-sequence regression
Why V4 as input?
  Central chest position
  Good correlation with V3, V5 (neighbors)
Challenge: V1 and V2 are far from V4 → hard to reconstruct
Notes: Chest leads can't be derived mathematically—they measure unique electrical activity from different chest positions. We chose V4 as input because it's central, but this creates a challenge for V1/V2 reconstruction.

## Slide 8
Neural Network: 1D U-Net Architecture
Architecture: Encoder-Decoder with Skip Connections
Encoder Path (Downsampling):
  Conv1D blocks: 3 → 64 → 128 → 256 → 512 channels
  MaxPool1D(2) reduces temporal dimension: 5000 → 2500 → 1250 → 625 → 312
Bottleneck: 1024 channels, captures multi-beat context
Decoder Path (Upsampling):
  ConvTranspose1D restores resolution
  Skip connections concatenate encoder features
  Channels: 1024 → 512 → 256 → 128 → 64 → 5
Output: [B, 5, 5000] (V1, V2, V3, V5, V6)
Notes: We use a 1D U-Net—classic encoder-decoder with skip connections, adapted for temporal signals. The encoder compresses, capturing multi-scale features. Skip connections preserve fine-grained temporal details like QRS spikes.

## Slide 9
Architecture Design Decisions
Design Choice | Decision | Rationale
Architecture | 1D U-Net | Skip connections preserve QRS spikes
Downsampling | MaxPool1d(2) | Preserves sharp peaks
Upsampling | ConvTranspose1d | Learnable upsampling
Normalization | BatchNorm | Stable training
Kernel Size | 3 | Captures 6ms local morphology
Dropout | 0.2 | Regularization
Depth | 4 levels | Full 10s receptive field
Notes: U-Net is ideal because skip connections preserve sharp QRS complexes. We chose U-Net over Transformers for computational efficiency—self-attention on 5000 timesteps is expensive.

## Slide 10
Ablation: Shared vs Lead-Specific Decoder
Metric | Shared Decoder | Lead-Specific | Winner
Parameters | 17.1M | 40.8M | Shared ✓
V1 Correlation | 0.726 | 0.734 | Lead-Specific
V2 Correlation | 0.683 | 0.639 | Shared ✓
V3 Correlation | 0.765 | 0.720 | Shared ✓
V5 Correlation | 0.824 | 0.772 | Shared ✓
V6 Correlation | 0.723 | 0.671 | Shared ✓
DL Mean | 0.744 | 0.707 | Shared ✓
Notes: Counter-intuitively, the simpler shared decoder wins on 4/5 leads despite 2.4x fewer parameters. With limited input information, parameter sharing acts as regularization.

## Slide 11
Training Configuration
Loss Function:
MSE on 5 DL leads only
L = (1/5) Σ MSE(ŷ_k, y_k)
Optimizer: AdamW
Learning Rate: 3×10⁻⁴
Weight Decay: 1×10⁻⁵
Batch Size: 64
Training Details:
Epochs: 150
Scheduler: ReduceLROnPlateau
Mixed Precision: FP16
Hardware:
GPU: NVIDIA A100 (40GB)
Training Time: 87 minutes
Code: run_training.py
Notes: We use MSE loss on the 5 DL leads only—physics leads are exact and don't need training. AdamW with weight decay provides L2 regularization.

## Slide 12
Dataset: PTB-XL
Source: PhysioNet (public)
Total ECGs: 21,837
Unique Patients: 18,885
Sampling Rate: 500 Hz
Duration: 10 seconds
Samples per Lead: 5,000
Diagnostic Labels (SNOMED-CT):
SR: Sinus Rhythm (normal)
MI: Myocardial Infarction
AF: Atrial Fibrillation
LBBB/RBBB: Bundle Branch Block
LVH: Left Ventricular Hypertrophy
Files: data/processed_full/
Notes: PTB-XL is the largest publicly available clinical ECG dataset. Each recording is 10 seconds at 500 Hz.

## Slide 13
Patient-Wise Data Splitting (Critical!)
The Problem:
  Some patients have multiple ECGs
  Record-wise splitting → same patient in train AND test
  Result: Data leakage → artificially inflated metrics
Our Solution:
  Split by PATIENT ID, not by record
  Each patient appears in only ONE split
Split Statistics:
  Train: 14,363 samples (70%)
  Validation: 3,086 samples (15%)
  Test: 3,086 samples (15%)
This is stricter but gives HONEST generalization estimates
Notes: This is a critical methodological point. Many prior works use record-wise splitting, which leaks patient information. We ensure each patient appears in only ONE split.

## Slide 14
Evaluation Metrics
Metric | Formula | Interpretation | Target
MAE | ¦y - ŷ¦ / N | Amplitude error (lower better) | < 0.05 mV
Pearson r | Cov(Y,Ŷ) / (σ_Y × σ_Ŷ) | Shape similarity [-1,1] | > 0.90
SNR (dB) | 10·log₁₀(¦¦y¦¦² / ¦¦y-ŷ¦¦²) | Signal quality (higher better) | > 20 dB
Notes: We use three complementary metrics. MAE captures amplitude error, correlation captures waveform shape similarity, and SNR gives a global signal quality measure.

## Slide 15
Results: Physics-Based Leads (Exact)
Lead | MAE | Correlation | SNR
III | 0.000 | 1.000 | ∞
aVR | 0.000 | 1.000 | ∞
aVL | 0.000 | 1.000 | ∞
aVF | 0.000 | 1.000 | ∞
Notes: For the physics-based leads, we achieve perfect reconstruction by definition. This is the key advantage of our hybrid approach.

## Slide 16
Results: Deep Learning Leads
Lead | MAE | Correlation | SNR (dB)
V1 | 0.036 | 0.726 | 17.9
V2 | 0.041 | 0.683 (worst) | 17.1
V3 | 0.036 | 0.765 | 17.8
V5 | 0.032 | 0.824 (best) | 18.7
V6 | 0.038 | 0.723 | 17.2
Mean | 0.037 | 0.744 | 17.8
Notes: V5 performs best (closest to V4 input). V2 performs worst (furthest from V4). All leads below clinical target of r > 0.90.

## Slide 17
Aggregate 12-Lead Performance
Overall Metrics (all 12 leads):
  Correlation: 0.893
  MAE: 0.0153
  SNR: 62.3 dB
But this is MISLEADING!
  Inflated by 3 input leads (trivially r=1.0)
  Inflated by 4 physics leads (exactly r=1.0)
Honest metric: DL leads average = 0.744
This is why we report per-component metrics!
File: models/model_comparison_metrics.json
Notes: The overall 0.893 looks good but is misleading. It's inflated by input and physics leads. The honest measure of our learning is the DL leads average: 0.744.

## Slide 18
Information Bottleneck Analysis
Target Lead | Best Input Corr. | Our Model r | Analysis
V1 | 0.49 (Lead I) | 0.726 | Model learns +0.24
V2 | 0.36 (V4) | 0.683 | Model learns +0.32
V3 | 0.71 (V4) | 0.765 | Near ceiling
V5 | 0.79 (V4) | 0.824 | Near ceiling
V6 | 0.69 (Lead I) | 0.723 | Model learns +0.03
Notes: V2's ground truth correlation with V4 is only 0.36. No model can perfectly reconstruct V2 from V4 because the information isn't there. Our 0.683 is actually impressive given this constraint.

## Slide 19
Comparison with State-of-the-Art
Method | Year | Chest r | Data Split
Linear (Frank) | 1970s | 0.70-0.75 | N/A
CNN (Sohn) | 2020 | 0.85 | Record-wise
LSTM (Lee) | 2021 | 0.88 | Record-wise
Transformer | 2023 | 0.90 | Record-wise
Ours | 2025 | 0.744 | Patient-wise
Notes: We're below SOTA on chest leads. But we use patient-wise splitting while most prior work uses record-wise—their metrics are likely inflated by data leakage.

## Slide 20
Gap Analysis: Why Below SOTA?
Three factors explain the performance gap:
1. Patient-wise splitting (stricter, more honest)
Prior work often uses record-wise splits
Data leakage inflates their metrics
2. Input lead choice (I, II, V4)
V4 has low correlation with V1/V2 (0.36-0.49)
Information bottleneck limits reconstruction
3. No data augmentation or pretrained weights
Our advantage: Physics guarantees + reproducible evaluation
Notes: The gap is primarily explained by our stricter evaluation methodology and the information bottleneck from our input lead choice.

## Slide 21
Key Findings
1. Physics constraints work perfectly
Limb leads: r = 1.0 guaranteed, eliminates error for 4/12 leads
2. Simpler models win with limited input
Shared decoder (17.1M) > Lead-specific (40.8M)
Parameter sharing = implicit regularization
3. Information bottleneck is the fundamental limit
V4 ↔ V2 correlation only 0.36 in ground truth
Model can't reconstruct what input doesn't contain
4. Input selection > architecture
Adding V2 as input would directly improve V2 reconstruction
Notes: Five key takeaways: physics works, simpler models win, information bottleneck limits us, input selection matters most.

## Slide 22
Limitations
1. Single Dataset
Only PTB-XL tested
Unknown generalization to other populations, devices, hospitals
2. Resting ECGs Only
No stress/exercise ECGs tested
3. Input Lead Dependency
Results specific to (I, II, V4) configuration
4. No Downstream Validation
Signal metrics only, no diagnostic classification test
5. No Uncertainty Quantification
Point estimates only, no confidence intervals
Notes: Important limitations: single dataset, no downstream diagnostic validation, no uncertainty quantification.

## Slide 23
Future Directions
1. Input Lead Optimization
Test: (I, II, V2), (I, II, V3), (I, II, V2+V4)
2. Uncertainty Quantification
Add probabilistic head (VAE, MC Dropout)
3. External Validation
Chapman-Shaoxing (China), MIMIC-IV-ECG (US)
4. Downstream Validation
Multi-label classification on reconstructed ECGs
Measure ΔAUROC for MI, AF, LVH detection
5. Foundation Model Approach
Self-supervised pretraining on millions of ECGs
Notes: Most important next step is testing different input leads. We also need downstream validation to prove clinical utility.

## Slide 24
Code Repository
GitHub: github.com/whiteblaze143/DATA_5000
Key Files:
  run_training.py: Main entry point
  src/train.py: Training loop
  src/physics.py: Einthoven/Goldberger equations
  src/models/unet_1d.py: U-Net architecture
  src/evaluation.py: Metrics computation
Data: data/processed_full/
Models: models/overnight_full/best_model.pt
Results: models/model_comparison_metrics.json
Notes: All code is available on GitHub. The key files are in src/ for the model and training, data/ for preprocessing, and models/ for trained checkpoints.

## Slide 25
Conclusion
What we built:
  Hybrid physics-informed deep learning system
  Reconstructs 12-lead ECG from 3 measured leads
What we achieved:
  ✓ Perfect limb lead reconstruction (r = 1.0) via physics
  △ Moderate chest lead reconstruction (r = 0.744) via U-Net
  ✓ Overall 12-lead correlation: 0.893
Key insight:
  Input lead selection is MORE important than model architecture
Clinical potential:
  Enable wearables to provide near-12-lead capability
Notes: Our hybrid approach successfully combines physics and deep learning. The physics component works perfectly. The DL component is limited by the information bottleneck.

## Slide 26
Questions?

## Slide 27
Thank You!
Repository: github.com/whiteblaze143/DATA_5000
Contact:
  Damilola Olaiya: damilolaolaiya@cmail.carleton.ca
  Mithun Mani: mithunmani@cmail.carleton.ca
Acknowledgments:
  DATA 5000 Course Instructors & TAs
  PhysioNet for PTB-XL dataset access